## Slide 1
7th Meeting of the S-100 Working Group
S-100 Validation Tests Workshop
Liz HAHESSY & Jonathan PRITCHARD
Agenda Item 8

## Slide 2: Objectives
Formation of Sub Working Group
  Lead: Liz Hahessy
  Volunteers – if want to participate email Yong Baek (yong.baek@iho.int) and Liz Hahessy (elihh@gst.dk)
  Agree next meeting
Consensus on different types of Validation
Explanation of background, existing work and discussion around potential issues. Develop understanding of the task and importance
Agree on next steps and actions
If time:
  Agree format structure for S-100 Validation Tests
  look at some of the existing proposed S-100 Validation tests

## Slide 3: What is required?
Validation tests between multiple product specifications, aimed at increasing the harmonisation of datasets and user experience of them for live navigation on the S-100 ECDIS.
  Need to ensure safe navigation whilst using multiple interoperable product specifications
    Safe = ECDIS Behaviour e.g. if alarms on S-102 must alarm on S-101
  Need to ensure data producers understand the implications of producing multiple product specifications
  Enable validation software to be produced that supports S-100 validation

## Slide 4: What is required?
  HSSC task – HSSC14/15
  Action:
  “For the same reasons as above, HSSC noted the slow progress on the development of a harmonized data validation process and associated catalogues across the S100 framework and agreed on the establishment of a dedicated subgroup.”
  Deadline:
  HSSC 15

## Slide 5: Why is it necessary?
Producing multiple datasets containing similar data that needs to interoperate and be safe for use
Not necessarily same model
Not same limits (no requirements for coincident/identical coverage)
May not be the same data producer
S-57 Band 4
S-57 Band 4
S-57 Band 3

## Slide 6: What is validation?
Current validation
Modelled from S-58
Integral part of IHO Standards
  S-58 ENC Validation Checks
    Cover semantic, formatting and structural aspects of S-57 ENC data
    Majority of tests carried out “within” the cell, without reference to other datasets or external data
  Horizontal & Vertical consistency checks are conducted by HOs and RENCs – most are not formalised

## Slide 7: What is validation?
Intra – cell validation
Inter – cell validation

## Slide 8: What is validation?
Intra-cell – Validation tests to ensure cell validates against itself
Inter-cell – Tests to ensure the cell validates against those it spatially intersects, touches or joins with
Intra
Inter
Now
S-100 Future
Intra
Inter
New dimension of validation

## Slide 9: What is validation
At a simple level there are 3 types of data validation tests (content)
  Inside cell
  Between adjoining cells
  Between product specifications for different types
Do we agree?
Responsibilities
  Inside the Product Specification - intra and inter - lies with Product Specification owners
  Outside - within this group?
    With support from Product Specification owners
    Is some of this temporary with the formation of an S-98 sub group?

## Slide 10: S-100 Validation
S-100 Framework
Product Specification
FC1
DCEG1
FC Schema
Geometry
Encoding (8211, GML, HDF5)
Dataset(s)
FC2
DCEG2
Dataset2
Dataset3
Dataset1
Interoperability
S-98
Interoperability Catalogue
CATALOG.XML1
S-128
f
a
b
c
d
e
g
j
h
i
Notes: Jonathan Pritchard diagram – different elements and types of validation
S-100 Framework at the top
2 Product Specifications (could be more) and their Feature Catalogues and DCEGs
Then Datasets made from these FC/ DCEG combinations
Notice there are dashed lines and arrows – these are the different types of validation which we will discuss next

## Slide 11
Validation | Against | Who? | Notes / Examples
a | Dataset against itself | Data Producer | Incorrect ordering of features
b | S-100 Geometry Schema | Data Producer | Things which contravene the geometry model, e.g clockwise/anticlockwise rings, unused curves
c | S-100 Encoding (Part 10a, b or c) | Data Producer | Formatting problem with encodings, corrupt ISO8211, non-conformant GML, incorrect HDF5 group names, incorrectly formatted attributes (e.g. dates, Booleans or unknowns), bad filenames
d | Product Specification Feature Catalogue | Data Producer | Names of attributes or features which aren’t in the feature catalogue. Missing mandatory attribution
e | Product Specification DCEG |  | Bad combination of attributes
f | Against other datasets of the same type | Aggregator | Horizontal/vertical consistency
g | Datasets of a different type | Aggregator | e.g. S-102 depths shoaler than S-101 depths
h | Part 17 Catalogue (and Part 15) | Aggregator | Bad digital signatures, coverage of dataset doesn’t match coverage in catalogue, incorrect encoding or mismatch of producer code
i | Corresponding S-128 | Distributor? | Mismatch of coverage or dataset name.
j | Against interoperability catalogue | Producer | Incomplete substituted layer (L2), mismatch of positions (L1)
Responsibilities:
  Who writes & maintains the different types of validation

## Slide 12
S-100 Conformance Tests
  Test dataset against FC
  Standard for all Product Specifications – so all S-100 level?
    Should that fall within PS validation or at S-100 validation level?

## Slide 13: Validation between product specifications
Is this group responsible for tests between PS?
If yes, focus on interoperability?
  Interleaves
  Replaces features – bigger implications
  How maintain onwards?
  Is this a temporary home until S-98 sub group set up?

## Slide 14: Progress so far
S-101 Project Team has reviewed S-58 and identified which validation tests are:
  Relevant to S-101 and carried forward
  Which tests are more generic S-100 tests
  Initially identified some new tests for S-101

## Slide 15: Progress so far…2
IIC Technologies have produced a Technical Report on Validation of S-100 datasets (Agenda item 8.1)
  Covers background to validation
  Beginning of description of ‘methodology’ of Validation
  Primarily looking at S-101, S-102, S-104 & S-111
  Proposed categorisation of S-100 Validation Tests
  Initial list of 45 tests (Primarily focused of S-101, S-102, S-104 & S-111)
  Testing validation of:
    S-102 against S-101 using UKHO test data (Isle of Wight)
    Working with US datasets to find examples of reconciling S-111 data with tidal data in S-101
https://iho.int/uploads/user/Services%20and%20Standards/S-100WG/S-100WG7/S100WG7-8.1_2022_EN_Validation%20Tests%20v7.3.0_Draft.pdf

## Slide 16: Progress so far…3
Summary of UKHO findings - wreck
S-101 Wreck feature (with a coincident Obstruction) with a valueOfSounding of 8.4m
S-102 value corresponding to the point feature (which is within the bounding rectangle of the S-102 point) is 8.39999961853027
Notes: A route has been plotted through the region and the S-102 data overlaid on ENC polygons and features. As part of this testing, a number of tests were run, including sanity tests of values, formats, HDF5 formatting and metadata examinations of coverage and grids.
In order to experiment with cross-product validation the depths in the ENC (as defined by the S-101 depth areas and valueOfSounding attributes were cross referenced against the 500k depth value points in the S-102 dataset. This involved using the rectangular extents of each S-102 point (as described in the previous section using linear interpolation) against DepthArea polygons and features with value of sounding value

## Slide 17: Progress so far…4
NOAA Sandy Hook – Interoperablity issues between products
S-102 with a user selected safety contour selected, however, the S-102 data was interpolated over land, so Sandy Hook is no longer visible on screen
S-102 Turned off

## Slide 18: Progress so far…5
Have other Test Beds or organisations starting working on S-100 Validation tests that they are willing to share?
  Production Software manufacturers
  Validation Software manufacturers
  RENCs
  OEMs
  Test Beds
  Data producers
  Others…

## Slide 19: What is the deliverable?
List of S-100 Validation Tests - is this a Part of S-100 or separate standard (S-158?)
  What is the format of these tests – propose use IICs suggestion to start with
  Explanatory section including description of what ‘Validation’ is
Recommendation of how we organise validation between different products – Is this S-98 now?
  How do, how record, how update/maintain
  Update S-97?
Guidance document for data producers?
  But not hold up factor
  Scope of work - is this limited in the first instance to Route Monitoring PSs?
  Link to DCEG?

## Slide 20: assumptions
S-101 must always be ‘safest’
  Do we need a definition
Must be possible to use S-101 ENC without additional S-xxx products
Do we need a generic list of assumptions and/or ones specific between product specifications?
Combination of products must be least as safe as individual
“After S-57 is no longer a live standard, the S-57 tests can be deleted from the test cases and documentation without any impact. Therefore, S-100 and S-57 datasets should be standalone (except where specific DF tests are planned/executed)” – S-164
  So want to keep S-58 & S-158 separate

## Slide 21: Proposed structure for tests
Categories:
Dataset Coverage and Datums
Data Values
Coverage
Grid Structure
Resolution
Dataset Metadata
Cross Validation
Propose adding Standard/document to refer to

## Slide 22: When is it required/ DEpendencies?
When required?
  Are there phases
  What is phase 1? Route Monitoring
What are S-100 Validation tests a dependency to?
  Product Specifications being ready for Ed. 2.0.0
    Generic tests & FC
    Revisit once Interoperability catalogue produced

## Slide 23: DEpendencies
Test data is required to test validation
  Potentially work with Test Beds and RENCs to start with
  Resources to test
  IHO Singapore Lab?
Link between S-164 and S-100 Validation Tests
  S-164 needs to be validated?
  Do we need S-164 datasets for S-100 Validation Tests?

## Slide 24: What work is required?
Initial work
  Establish GitHub page
  Identifying which scenarios require validation & who responsible
    Identifying who to contact
  Agree to use IICs test structure?
  Insert S-101 PT S-100 tests into new structure
  Start producing simple document explaining:
    ‘What validation is’
    How it is structured
    Identifying responsibilities for different parts of validation
  Review Governance Docs gaps
  Session at TSM
  Request S-158
Further work
  Identify other S-100 Validation tests – do we need a full review?
  Potentially set up a test scenario for users/ Test beds to test and report back issues found

## Slide 25: Sum up
Establish list of volunteers – contact WG/PS owners not present
Next meeting
VTC correspondence group
  1st meeting beginning of February? (S-101to S-57 conversion meeting end Jan)
  How regularly meet? Monthly?
  Test Strategy Meeting in early March
  HSSC meeting June
Maintenance / Updating regime